Z80 Assembly
for the
Lesson 11: Intro to Graphics

---
Graphics Characters
- BASIC: Graphics input mode
- Each character: 2x2 bitmap of quasi-pixels
  - Quasi-pixel: 4x4 square of actual pixels
    - Full Display: 64x48 quasi-pixels
  - 2 colors: Paper and Ink, same brightness

---
Graphics Character Codes
- $80-$8F:
- G Cursor: 8 1 2 3 4 5 6 7 ↑7 ↑6 ↑5 ↑4 ↑3 ↑2 ↑1 ↑8
- Example:
  ld a,$10 ; INK
  rst $10
  ld a,1 ; blue
  rst $10
  ld a,$11 ; PAPER
  rst $10
  ld a,6 ; yellow
  rst $10
  ld a,$83 ; upper half ink
  rst $10

---
ZX Spectrum 48k Memory Map
0000	ROM	16 kB
3FFF
4000	Screen Bitmap (256x192)	6 kB
57FF
5800	Screen Color Attributes (32x24)	768 Bytes
5AFF
5B00	Reserved for BASIC	1.20 kB
5CCA
5CCB	Contended User RAM	8.80 kB
7FFF
8000	Free User RAM	31.84 kB
FF57
FF58	User-Defined Graphics (UDG)	168 Bytes
FFFF

---
User-Defined Graphics (UDG)
- 21 8x8 Bitmaps stored in RAM $FF58 to $FFFF
- Startup: “A” through “U” bitmaps copied from ROM
- Codes $90 (A) to $A4 (U)
- Example:
  UDG_O_CODE = $9E
  UDG_O_BITMAP = $FFC8
  ld a,UDG_O_CODE
  rst $10
  ld a,%00111100
  ld (UDG_O_BITMAP+3),a
  ld a,UDG_O_CODE
  rst $10

---
Direct Screen Access
- Bitmap: $4000 to $57FF
- Attributes: $5800 to $5AFF
ROM
Screen
RAM
ULA
Z80
User RAM

---
Bitmap Addressing
- For Pixel X,Y:
  - X = X7…X0
  - Y = Y7…Y0
  - Pixel Address =
    - Each byte = 8 pixels in line, MSB = left end
  - Increment Address Low Byte:
    - Increment X by 8 within line
  - Increment Address High Byte:
    - Increment Y by 1 within 8-line character row
0	1	0	Y7	Y6	Y2	Y1	Y0	Y5	Y4	Y3	X7	X6	X5	X4	X3

---
Set A Pixel
Input: B = X coord.; C = Y coord.
setpixel: ld a,c ld h,a
   ld a,b and $38 ld a,$00
   and $07 sla a scf
   ld d,a sla a sp_loop:
   ld l,b or l rra
   srl l ld l,a dec d
   srl l ld a,c jp p,sp_loop
   srl l and $C0 or (hl)
   ld a,c srl a ld (hl),a
   and $07 srl a ret
   or $40 srl a
   ld h,a or h
0	1	0	Y7	Y6	Y2	Y1	Y0	Y5	Y4	Y3	X7	X6	X5	X4	X3

---
Attribute Addressing
- For Pixel X,Y:
  - TileX = floor(X/8)
  - TileY = floor(Y/8)
  - Tile Attribute Address = $5800 + TileY*32 + TileX
- Tile attributes apply to all 64 pixels in tile
- 1 attribute byte per tile:
Flash	Bright	Paper2	Paper1	Paper0	Ink2	Ink1	Ink0

---
Spectrum Color Palette
8 colors x 2 brightness levels

---
Example Program
- Graphics Via 4 Methods:
  - Fixed Graphics Characters
  - User-Defined Graphics Characters (UDG)
  - Bitmap Loading
  - Programmatic Bitmap Manipulation

---
        UDG_0 UDG_1 UDG_2
    UDG_3 UDG_4 UDG_5 UDG_6 UDG_7
        UDG_8 UDG_9