Z80 Assembly
for the
Lesson 2: Addressing Modes

---
ZX Spectrum 48k Memory Map
0000	ROM	16 kB
3FFF
4000	Screen Bitmap (256x192)	6 kB
57FF
5800	Screen Color Attributes (32x24)	768 Bytes
5AFF
5B00	Reserved for BASIC	1.20 kB
5CCA
5CCB	Contended User RAM	8.80 kB
7FFF
8000	Free User RAM	31.84 kB
FF57
FF58	User-Defined Graphics (UDG)	168 Bytes
FFFF

---
Z80 Architecture
A
F
A’
F’
B
C
B’
C’
D
E
D’
E’
H
L
H’
L’
SP
PC
IX
IY
I
R

---
Implied Addressing
- No operands in assembly or machine code
- May affect registers and/or memory
        nop halt
        di ei
        ret exx
        rla ldir

---
“Load” Mnemonic Syntax
LD destination,source
; Assembly: C:
  ld a,42 ; A = 42
  ld ($89AB),a ; *(0x89AB) = A
  ld (hl),d ; *HL = D
  ld bc,($CDEF) ; BC = *(0xCDEF)
  ld a,(bc) ; A = *BC

---
Register Addressing
Reads or writes value of register
ld a,i ld ixh,ixl ex af,af’
ld b,c ld iyh,iyl push bc
ld d,e ld sp,hl pop de
ld h,l ld sp,ix in f,(c)
ld r,a ld sp,iy

---
Immediate Addressing
- Use 8-bit value in code
- No memory fetch after instruction fetch
ld a,42
ld b,%00101010
ld c,$2A
cp 123

---
Extended Immediate Addressing
- Use 16-bit value in code
- No memory fetch after instruction fetch
        ld bc,4660
        ld de,%0001001000110100
        ld hl,$1234
        jp $89AB

---
Extended (Direct) Addressing
- Read or write value in memory at 16-bit address in code
- Value may be 8 or 16 bits, depending on other operand
     ld a,($1234) ; 8-bit read
     ld ($5678),a ; 8-bit write
     ld de,($9ABC) ; 16-bit read
     ld ($DEF0),hl ; 16-bit write

---
Register Indirect Addressing
- Reads or writes value in memory at address in register
- 16-bit register name in parentheses
   ld hl,$1234
   ld a,(hl)
Other examples:
       ld (bc),a ex (sp),hl
       ld a,(de) inc (hl)
} same as ld a,($1234)

---
Modified Page Zero Addressing
- Reference first memory page ($0000 to $00FF) by using only low byte of address ($00 to $FF)
- Only used by RST, and only for 8 specific addresses, specified by opcode (no machine code operand)
        rst $00 rst $20
        rst $08 rst $28
        rst $10 rst $30
        rst $18 rst $38

---
Relative Addressing
- Reference nearby address by 8-bit offset
  - PC change of -128 to +127
  - Assembler calculates offset from label
  - Assembly will fail if label is too distant
        label:
        djnz label
        jr z,label

---
Indexed Addressing
- Read or writes value in memory at offset from address in an index register (IX or IY)
  - Offset range: -128 to +127
- Does not affect value in index register
        ld a,(ix+11)
        ld (iy-103),b

---
Bit Addressing
- Read or writes specific bit in register or memory byte
  - Range:
- Other 7 bits ignored and unchanged
        bit 1,a
        set 3,(hl)
        res 6,(ix+42)
7	6	5	4	3	2	1	0

---
Condition
Executed only during specific status flag state
  jp c,$5678 ; carry bit set (C = 1)
  ret nc ; carry bit reset (C = 0)
  call z,$1234 ; zero bit set (Z = 1)
  jp nz,$9ABC ; zero bit reset (Z = 0)
  ret m ; sign bit set (S = 1)
  call p,$DEF0 ; sign bit reset (S = 0)
  jp pe,$2468 ; overflow bit set (P/V = 1)
  jp po,$3579 ; overflow bit reset (P/V = 0)

---
Interrupt Mode
- Only for IM instruction
- Range: 0, 1 or 2
  - Specified by opcode (no machine code operand)
  im 0 ; Interrupt Mode 0 = Peripheral-specified
       ; (not supported by ZX Spectrum)
  im 1 ; Interrupt Mode 1 = Fixed at $0038
  im 2 ; Interrupt Mode 2 = Vector table (Page = I)

---
Example Program
- Let’s just…
- Result: print some text