Z80 Assembly
for the
Lesson 3: Data in Motion

---
“Load” Mnemonic Syntax
LD destination,source
; Assembly: C:
  ld a,42 ; A = 42
  ld ($89AB),a ; *(0x89AB) = A
  ld (hl),d ; *HL = D
  ld bc,($CDEF) ; BC = *(0xCDEF)
  ld a,(bc) ; A = *BC

---
Z80 Architecture
A
F
A’
F’
B
C
B’
C’
D
E
D’
E’
H
L
H’
L’
SP
PC
IX
IY
I
R

---
ZX Spectrum 48k Memory Map
0000	ROM	16 kB
3FFF
4000	Screen Bitmap (256x192)	6 kB
57FF
5800	Screen Color Attributes (32x24)	768 Bytes
5AFF
5B00	Reserved for BASIC	1.20 kB
5CCA
5CCB	Contended User RAM	8.80 kB
7FFF
8000	Free User RAM	31.84 kB
FF57
FF58	User-Defined Graphics (UDG)	168 Bytes
FFFF

---
Hardware Ports
- Input/Output devices mapped to 8-bit Port Addresses
  - Port Address: Lower 8-bits of address bus
  - Upper 8-bits of address bus may also be used during I/O request
- ULA: Port $FE
  - Keyboard
  - Tape I/O
  - Piezoelectric Beeper

---
LD: LoaD
- Operands: Destination, Source
- 139 Opcodes!
- 8-bit Register-to-Register:
Source
Destination

---
LD: LoaD
- 16-bit Register-to-Register:
  - ld sp,hl	ld sp,ix	ld sp,iy

---
Example Program
Use LD, EX, EXX, LDI, LDD, LDIR, LDDR