Z80 Assembly
for the
Lesson 7: Bit by Bit

---
What’s a bit?
- True or False
  - High or Low
  - 1 or 0
- 00000000 = 0
- 11111111 = 255
 1 0 1 1 0 0 1 0
   7 6 5 4 3 2 1 0

---
Boolean Logic
- George Boole (1815-1864)
- 0 = False, 1 = True
Not
A	~A
0	1
1	0
Or
A	B	A ⋁ B
0	0	0
0	1	1
1	0	1
1	1	1
And
A	B	A ⋀ B
0	0	0
0	1	0
1	0	0
1	1	1
Exclusive Or
A	B	A ⊕ B
0	0	0
0	1	1
1	0	1
1	1	0

---
CPL: ComPLement
- AOUT = ~AIN
- Example:
  ld a,%00101010
  cpl ; A = %11010101
- N = 1
- H = 1
- All other flags unaffected

---
OR
- AOUT = AIN ⋁ Operand
- Supported Operands:
  - Register: A, B, C, D, E, H, L, IXH, IXL, IYH, IYL
  - Register Indirect: (HL)
  - Indexed: (IX+n), (IY+n)
  - Immediate: Any 8-bit value
- C = 0; N = 0; H = 0; P/V = Parity; S = AOUT bit 7; Z = AOUT == 0
  ld a,%00101010
  or %01011100 ; A = %01111110

---
AND
- AOUT = AIN ⋀ Operand
- Supported Operands:
  - Immediate: Any 8-bit value
- C = 0; N = 0; H = 0; P/V = Parity; S = AOUT bit 7; Z = AOUT == 0
  ld a,%00101010
  and %01011100 ; A = %00001000

---
XOR: eXclusive OR
- AOUT = AIN ⊕ Operand
- Supported Operands:
  - Immediate: Any 8-bit value
- C = 0; N = 0; H = 0; P/V = Parity; S = AOUT bit 7; Z = AOUT == 0
  ld a,%00101010
  xor %01011100 ; A = %01110110

---
Shifting
- Shifting to left: multiplication by 2
  - 00101010 → 01010100
    - 42 → 84
  - RIN = B7B6B5B4B3B2B1B0 →
    - COUT = B7; ROUT = B6B5B4B3B2B1B0[0|1|CIN|B7]
- Shifting to right: division by 2
  - 00101010 → 00010101
    - 42 → 21
  - RIN = B7B6B5B4B3B2B1B0 →
    - ROUT = [0|B7|CIN|B0]B7B6B5B4B3B2B1; COUT = B0

---
SLA: Shift Left Arithmetic
- Shifts byte one bit to left, filling with zero
- Supported Operands:
- OpOUT = OpIN << 1
- C = OpIN[Bit 7]; N = 0; H = 0; P/V = Parity; S = OpOUT bit 7; Z = OpOUT == 0
  ld a,%10101010
  sla a ; A = %01010100, carry set

---
SRA: Shift Right Arithmetic
- Shifts byte one bit to right, bit 7 unchanged
- Supported Operands:
- OpOUT = (OpIN >> 1) ⋁ (OpIN ⋀ %10000000)
- C = OpIN[Bit 0]; N = 0; H = 0; P/V = Parity; S = OpOUT bit 7; Z = OpOUT == 0
  ld a,%10101010
  sra a ; A = %11010101, carry clear

---
SRL: Shift Right Logical
- Shifts byte one bit to right, fill with zero
- Supported Operands:
- OpOUT = OpIN >> 1
- C = OpIN[Bit 0]; N = 0; H = 0; P/V = Parity; S = OpOUT bit 7; Z = OpOUT == 0
  ld a,%10101010
  srl a ; A = %01010101, carry clear

---
SLL: Shift Left Logical
- Shifts byte one bit to left, filling with 1
- Supported Operands:
- OpOUT = (OpIN << 1) ⋁ 1
- C = OpIN[Bit 7]; N = 0; H = 0; P/V = Parity; S = OpOUT bit 7; Z = OpOUT == 0
  ld a,%10101010
  sll a ; A = %01010101, carry set
UNDOCUMENTED

---
Rotating
- Rotating = Shifting, filling with carry flag
- Rotate Left
  - RIN = B7B6B5B4B3B2B1B0 →
    COUT = B7; ROUT = B6B5B4B3B2B1B0[CIN]
- Rotate Right
  - RIN = B7B6B5B4B3B2B1B0 →
    ROUT = [CIN]B7B6B5B4B3B2B1; COUT = B0
- Example: Multiply BC by 2
  sla c
  rl b

---
RR: Rotate Right
- Shifts byte one bit to right, fill with carry
- Supported Operands:
- OpOUT = (OpIN >> 1) ⋁ (CIN << 7)
- C = OpIN[Bit 0]; N = 0; H = 0; P/V = Parity; S = OpOUT bit 7; Z = OpOUT == 0
- RRA: Same as “RR A”, but S and Z preserved
  scf
  ld a,%10101010
  srl a ; A = %11010101, carry clear

---
RL: Rotate Left
- Shifts byte one bit to left, filling with carry
- Supported Operands:
- OpOUT = (OpIN << 1) ⋁ CIN
- C = OpIN[Bit 7]; N = 0; H = 0; P/V = Parity; S = OpOUT bit 7; Z = OpOUT == 0
- RLA: Same as “RL A”, but S and Z preserved
  scf
  ld a,%10101010
  rl a ; A = %01010101, carry set

---
RRC: Rotate Right Carry
- Shifts byte one bit to right, fill with previous bit 0
- Supported Operands:
- OpOUT = (OpIN >> 1) ⋁ ((OpIN ⋀ 1) << 7)
- C = OpIN[Bit 0]; N = 0; H = 0; P/V = Parity; S = OpOUT bit 7; Z = OpOUT == 0
- RRCA: Same as “RRC A”, but S and Z preserved
  ld b,%10101010
  rrc b ; B = %01010101, carry clear

---
RLC: Rotate Left Carry
- Shifts byte one bit to left, filling with previous bit 7
- Supported Operands:
- OpOUT = (OpIN << 1) ⋁ ((OpIN ⋀ %10000000) >> 7)
- C = OpIN[Bit 7]; N = 0; H = 0; P/V = Parity; S = OpOUT bit 7; Z = OpOUT == 0
- RLCA: Same as “RLC A”, but S and Z preserved
  ld b,%10101010
  rlc b ; B = %01010101, carry set

---
Decimal Rotation
- Rotates three nybbles between A and (HL)
- RLD: Rotate Left Decimal
  - Example:
    ld a,$09
    ld (hl),$42
    rld ; A = $04, (HL) = $29
- RRD Rotate Right Decimal
  - Example:
    ld a,$09
    ld (hl),$42
    rrd ; A = $02, (HL) = $94

---
Bit Addressing
- Read or writes specific bit in register or memory byte
  - Range:
- Other 7 bits ignored and unchanged
        bit 1,a
        res 3,(hl)
        set 6,(ix+42)
7	6	5	4	3	2	1	0

---
BIT
- Tests specified bit
- First Operand: Bit number to test (0-7)
- Second Operand: Byte to test
- Tested byte unaffected
- Z = Tested Bit Clear; N = 0; H = 1; Other flags preserved
  ld b,%10101010
  bit 4,b ; Z set
  bit 3,b ; Z clear

---
RES: RESet
- Clears specified bit
- First Operand: Bit number to clear (0-7)
- Second Operand: Byte to change
- Op2OUT = Op2IN ⋀ ~(1 << Op1)
- All flags preserved
  ld b,%10101010
  res 3,b ; B = %10100010

---
SET
- Sets specified bit
- First Operand: Bit number to set (0-7)
- Second Operand: Byte to change
- Op2OUT = Op2IN ⋁ (1 << Op1)
- All flags preserved
  ld b,%10101010
  set 4,b ; B = %10111010

---
Example Program
- Perform bitwise operations
- Print register contents