Z80 Assembly
for the
Lesson 7: Bit by Bit

---
CALL Effects
- Unconditional:
  - PCOUT = operand
- Conditional and taken:
  - PCOUT = second operand
- Unconditional OR conditional and taken:
  - SPOUT = SPIN – 2
  - (SPOUT) = PCIN + 3
- Conditional and not taken:
  - PCOUT = PCIN + 3

---
RST – call ReSTart
- Shortcut for calling special routines on page zero
- Operand: 8-bit address (upper byte zero)
  - Supported Addresses: $00, $08, $10, $18, $20, $28, $30, $38
- Effects:
  - PCOUT = operand
  - SPOUT = SPIN – 2
  - (SPOUT) = PCIN + 1

---
RET Effects
- Unconditional OR conditional and taken:
  - PCOUT = (SPIN)
  - SPOUT = SPIN + 2
- Conditional and not taken:
  - PCOUT = PCIN + 1

---
PUSH
- Pushes register value to stack
- Supported registers: AF, BC, DE, HL, IX, IY
- Example: push hl
  - Effects:
    - SPOUT = SPIN – 2
    - (SPOUT) = L
    - (SPOUT + 1) = H

---
POP
- Pops value off stack, stores it in register
- Supported registers: AF, BC, DE, HL, IX, IY
- Example: pop hl
  - Effects:
    - L = (SPIN)
    - H = (SPIN + 1)
    - SPOUT = SPIN + 2
- Flags unaffected unless AF is popped, and flag values are retrieved from stack

---
RETI – RETurn from Interrupt
- Unconditionally returns from Mode 2 interrupt routine
  - Interrupt Modes 0 and 1 use normal RET instructions
- Effects:
  - PCOUT = (SPIN)
  - SPOUT = SPIN + 2

---
RETN – RETurn from Non-maskable Interrupt
- Unconditionally returns from non-maskable interrupt (NMI) routine
- Effects:
  - Re-enables maskable interrupts
  - PCOUT = (SPIN)
  - SPOUT = SPIN + 2

---
One Byte at a Time
- Individual bytes can be “pushed” and “popped”
- Example: Push and pop only A – not AF
sp_backup:
dw 0
MACRO PUSH_A MACRO POP_A
   dec sp ld (sp_backup),sp
   ld (sp_backup),sp inc sp
   ld hl,(sp_backup) ld hl,(sp_backup)
   ld (hl),a ld a,(hl)
ENDM ENDM

---
Hot Swapping
- Last word pushed to stack can be exchanged with register value
  - HL, IX, IY
- Example: Switch values between BC and HL via the stack
ld bc,$1234
ld hl,$5678
push bc
ex (sp),hl ; HL = $1234
pop bc ; BC = $5678

---
Example Program
- Perform bitwise operations
- Print register contents