Z80 Assembly
for the
Lesson 4: Conditionality

---
Z80 Status Flags
S	Z	B5	H	B3	P/V	N	C
- F Register:
  - S: Signed – Value in A is negative
  - Z: Zero – Value in A is zero
  - B5: Bit 5 of last 8-bit opcode that altered flags
  - H: Half-Carry – Overflow occurred with lower nybble
  - B3: Bit 3 of last 8-bit opcode that altered flags
  - P/V: Parity/Overflow – Parity bit or overflow occurred
  - N: Add/Subtract – Subtract occurred since last add
  - C: Carry – Bit to carry to next operation

---
Z80 Status Flags
S	Z	B5	H	B3	P/V	N	C
- F Register:
  - S: Signed – Value in A is negative
  - Z: Zero – Value in A is zero
  - B5: Bit 5 of last 8-bit opcode that altered flags
  - H: Half-Carry – Overflow occurred with lower nybble
  - B3: Bit 3 of last 8-bit opcode that altered flags
  - P/V: Parity/Overflow – Parity bit or overflow occurred
  - N: Add/Subtract – Subtract occurred since last add
  - C: Carry – Bit to carry to next operation

---
Condition Mnemonic
- Used as first operand for all conditional assembly instructions
  - C - carry bit set (C = 1)
  - NC - carry bit reset (C = 0)
  - Z - zero bit set (Z = 1)
  - NZ - zero bit reset (Z = 0)
  - M - sign bit set (S = 1)
  - P - sign bit reset (S = 0)
  - PE - overflow bit set (P/V = 1)
  - PO - overflow bit reset (P/V = 0)

---
JP: JumP
- Jump PC to absolute address
- Unconditional: Always jump
  - Extended Immediate: jp $89AB
  - Register Indirect: jp (hl) . jp (ix) . jp (iy)
- Conditional: Jump if condition is true
  - Supported conditions: C, NC, Z, NZ, M, P, PE, PO
  - Target must be Extended Immediate address
  - Example: jp nz,$CDEF

---
Simple Looping
- Initialize loop index, decrement until Z bit set
- Case Study: Multiply value in accumulator by 32 (25)
  ld b,5
  loop:
  sla a
  dec b
  jp nz,loop

---
CP: ComPare
- Compares value in accumulator to another
- Sets flags based on sign and comparison
- Register Mode: Compare A with A, B, C, D, E, H, L, IXH, IXL, IYH, IYL
  - Example: cp b
- Immediate Mode: Compare A with 8-bit value
  - Example: cp 42
- Register Indirect: cp (hl)
- Indexed: cp (ix+101) . cp (iy-57)

---
CP: ComPare
- Result of comparison (N = value from operand):
  - A == N: Z = 1
  - A != N: Z = 0
  - A < N: C = 1
  - A >= N: C = 0

---
JR: Jump Relative
- Jump to relative address
  - Target address must be 8-bit offset from next instruction
- Unconditional: Always jump
  - Example: jr label
- Conditional: Jump if condition is true
  - Supported conditions: C, NC, Z, NZ
  - Example: jr c,label

---
RET: RETurn
- Returns from program or subroutine
- Unconditional (no operand): Always return
- Conditional: Return if condition is true
  - Supported conditions: C, NC, Z, NZ, M, P, PE, PO
  - Example: ret m

---
If/Else Implementation
- Use CP and conditional JR and RET to implement if/else branching
- Case Study: Normalize value towards 42
  in C: in Z80 Assembly:
  if (foo != 42) { ld a,(foo)
  if (foo < 42) { cp 42
  foo++; ret z
  } else { jr nc,toohigh
  foo--; inc a
  } jr done
  } toohigh:
  return; dec a
  done:
  ld (foo),a
  ret

---
CALL
- Call subroutine at absolute address
- PC jumps to address and execution continues until return
- Next instruction called after return
- Unconditional: Always call subroutine
  - Example: call $89AB
- Conditional: Call if condition is true
  - Supported conditions: C, NC, Z, NZ, M, P, PE, PO
  - Example: call pe,$CDEF

---
CCF/SCF – Clear/Set Carry Flag
- Explicitly set the state of the carry flag (C)
- CCF: Set C to 0
- SCF: Set C to 1
- Affects no other flags

---
DJNZ – Decrement and Jump if Not Zero
- Decrements B
- If B is not zero after decrement, jump to relative address
- Does not affect any flags (Not even Z!)
- Example: djnz label

---
Example Program
- Use conditional instructions to control program flow
- Print string three ways:
  - Original
  - All lowercase
  - All uppercase