Z80 Assembly
for the
Lesson 5: Arithmetic

---
8-Bit Arithmetic: C vs. Assembly
- C: Fortran-like mathematical operations
- Assembly: Add, subtract, shift, rotate
Assembly:
C:
val = foo + bar – baz;
   ld a,(bar)
   ld b,a
   ld a,(baz)
   ld c,a
   ld a,(foo)
   add a,b
   sub c
   ld (val),a

---
ADD (8-Bit)
- Adds value of second operand to accumulator
- First Operand: Always A
- Second Operand:
  - Register:
    - A, B, C, D, E, H, L, IXH, IXL, IYH, IYL
  - Register Indirect:
    - (HL)
  - Indexed:
    - (IX+n), (IY+n)
  - Immediate
    - Example: add a,42

---
ADD (8-Bit) Effects
- Sum = AIN + Op2
- AOUT = Sum % 256
- S = AOUT > 127 (negative if A interpreted as signed 8-bit integer)
- Z = AOUT == 0
- H = (AIN % 16) + (Op2 % 16) > 15
- P/V = (SumSIGNED < -128) || (SumSIGNED > 127)
  - Sum of two “negative” or two “positive” values doesn’t fit A
- N = 0
- C = Sum > 255

---
Let’s Accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld a,42
ld b,220
add a,b
add a,b
add a,b
ld b,42
add a,b
ld b,128
add a,b
ld b,42
add a,b
ld b,110
add a,b

---
Let’s Accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld a,42	42	42	2A	?	?	?	?	?	?	?	?	?
ld b,220
add a,b
add a,b
add a,b
ld b,42
add a,b
ld b,128
add a,b
ld b,42
add a,b
ld b,110
add a,b

---
Let’s Accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,220	42	42	2A	220	-36	DC	?	?	?	?	?	?
add a,b
add a,b
add a,b
ld b,42
add a,b
ld b,128
add a,b
ld b,42
add a,b
ld b,110
add a,b

---
Let’s Accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,220	42	42	2A	220	-36	DC	?	?	?	?	?	?
add a,b	6	6	06	220	-36	DC	0	0	1	0	0	1
add a,b
add a,b
ld b,42
add a,b
ld b,128
add a,b
ld b,42
add a,b
ld b,110
add a,b

---
Let’s Accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,220	42	42	2A	220	-36	DC	?	?	?	?	?	?
add a,b	6	6	06	220	-36	DC	0	0	1	0	0	1
add a,b	226	-30	E2	220	-36	DC	1	0	1	0	0	0
add a,b
ld b,42
add a,b
ld b,128
add a,b
ld b,42
add a,b
ld b,110
add a,b

---
Let’s Accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,220	42	42	2A	220	-36	DC	?	?	?	?	?	?
add a,b	6	6	06	220	-36	DC	0	0	1	0	0	1
add a,b	226	-30	E2	220	-36	DC	1	0	1	0	0	0
add a,b	190	-66	BE	220	-36	DC	1	0	0	0	0	1
ld b,42
add a,b
ld b,128
add a,b
ld b,42
add a,b
ld b,110
add a,b

---
Let’s Accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,220	42	42	2A	220	-36	DC	?	?	?	?	?	?
add a,b	6	6	06	220	-36	DC	0	0	1	0	0	1
add a,b	226	-30	E2	220	-36	DC	1	0	1	0	0	0
add a,b	190	-66	BE	220	-36	DC	1	0	0	0	0	1
ld b,42	190	-66	BE	42	42	2A	1	0	0	0	0	1
add a,b
ld b,128
add a,b
ld b,42
add a,b
ld b,110
add a,b

---
Let’s Accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,220	42	42	2A	220	-36	DC	?	?	?	?	?	?
add a,b	6	6	06	220	-36	DC	0	0	1	0	0	1
add a,b	226	-30	E2	220	-36	DC	1	0	1	0	0	0
add a,b	190	-66	BE	220	-36	DC	1	0	0	0	0	1
ld b,42	190	-66	BE	42	42	2A	1	0	0	0	0	1
add a,b	232	-24	E8	42	42	2A	1	0	1	0	0	0
ld b,128
add a,b
ld b,42
add a,b
ld b,110
add a,b

---
Let’s Accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,220	42	42	2A	220	-36	DC	?	?	?	?	?	?
add a,b	6	6	06	220	-36	DC	0	0	1	0	0	1
add a,b	226	-30	E2	220	-36	DC	1	0	1	0	0	0
add a,b	190	-66	BE	220	-36	DC	1	0	0	0	0	1
ld b,42	190	-66	BE	42	42	2A	1	0	0	0	0	1
add a,b	232	-24	E8	42	42	2A	1	0	1	0	0	0
ld b,128	232	-24	E8	128	-128	80	1	0	1	0	0	0
add a,b
ld b,42
add a,b
ld b,110
add a,b

---
Let’s Accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,220	42	42	2A	220	-36	DC	?	?	?	?	?	?
add a,b	6	6	06	220	-36	DC	0	0	1	0	0	1
add a,b	226	-30	E2	220	-36	DC	1	0	1	0	0	0
add a,b	190	-66	BE	220	-36	DC	1	0	0	0	0	1
ld b,42	190	-66	BE	42	42	2A	1	0	0	0	0	1
add a,b	232	-24	E8	42	42	2A	1	0	1	0	0	0
ld b,128	232	-24	E8	128	-128	80	1	0	1	0	0	0
add a,b	104	104	68	128	-128	80	0	0	0	1	0	1
ld b,42
add a,b
ld b,110
add a,b

---
Let’s Accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,220	42	42	2A	220	-36	DC	?	?	?	?	?	?
add a,b	6	6	06	220	-36	DC	0	0	1	0	0	1
add a,b	226	-30	E2	220	-36	DC	1	0	1	0	0	0
add a,b	190	-66	BE	220	-36	DC	1	0	0	0	0	1
ld b,42	190	-66	BE	42	42	2A	1	0	0	0	0	1
add a,b	232	-24	E8	42	42	2A	1	0	1	0	0	0
ld b,128	232	-24	E8	128	-128	80	1	0	1	0	0	0
add a,b	104	104	68	128	-128	80	0	0	0	1	0	1
ld b,42	104	104	68	42	42	2A	0	0	0	1	0	1
add a,b
ld b,110
add a,b

---
Let’s Accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,220	42	42	2A	220	-36	DC	?	?	?	?	?	?
add a,b	6	6	06	220	-36	DC	0	0	1	0	0	1
add a,b	226	-30	E2	220	-36	DC	1	0	1	0	0	0
add a,b	190	-66	BE	220	-36	DC	1	0	0	0	0	1
ld b,42	190	-66	BE	42	42	2A	1	0	0	0	0	1
add a,b	232	-24	E8	42	42	2A	1	0	1	0	0	0
ld b,128	232	-24	E8	128	-128	80	1	0	1	0	0	0
add a,b	104	104	68	128	-128	80	0	0	0	1	0	1
ld b,42	104	104	68	42	42	2A	0	0	0	1	0	1
add a,b	146	-110	92	42	42	2A	1	0	1	1	0	0
ld b,110
add a,b

---
Let’s Accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,220	42	42	2A	220	-36	DC	?	?	?	?	?	?
add a,b	6	6	06	220	-36	DC	0	0	1	0	0	1
add a,b	226	-30	E2	220	-36	DC	1	0	1	0	0	0
add a,b	190	-66	BE	220	-36	DC	1	0	0	0	0	1
ld b,42	190	-66	BE	42	42	2A	1	0	0	0	0	1
add a,b	232	-24	E8	42	42	2A	1	0	1	0	0	0
ld b,128	232	-24	E8	128	-128	80	1	0	1	0	0	0
add a,b	104	104	68	128	-128	80	0	0	0	1	0	1
ld b,42	104	104	68	42	42	2A	0	0	0	1	0	1
add a,b	146	-110	92	42	42	2A	1	0	1	1	0	0
ld b,110	146	-110	92	110	110	6E	1	0	1	1	0	0
add a,b

---
Let’s Accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,220	42	42	2A	220	-36	DC	?	?	?	?	?	?
add a,b	6	6	06	220	-36	DC	0	0	1	0	0	1
add a,b	226	-30	E2	220	-36	DC	1	0	1	0	0	0
add a,b	190	-66	BE	220	-36	DC	1	0	0	0	0	1
ld b,42	190	-66	BE	42	42	2A	1	0	0	0	0	1
add a,b	232	-24	E8	42	42	2A	1	0	1	0	0	0
ld b,128	232	-24	E8	128	-128	80	1	0	1	0	0	0
add a,b	104	104	68	128	-128	80	0	0	0	1	0	1
ld b,42	104	104	68	42	42	2A	0	0	0	1	0	1
add a,b	146	-110	92	42	42	2A	1	0	1	1	0	0
ld b,110	146	-110	92	110	110	6E	1	0	1	1	0	0
add a,b	0	0	00	110	110	6E	0	1	1	0	0	1

---
SUB: SUBtract
- Subtracts value of operand from accumulator
- Register:
  - A, B, C, D, E, H, L, IXH, IXL, IYH, IYL
- Register Indirect:
  - (HL)
- Indexed:
  - (IX+n), (IY+n)
- Immediate
  - Example: sub 42

---
SUB Effects
- Diff = AIN - Op
- AOUT = Diff % 256
- S = AOUT > 127 (negative if A interpreted as signed 8-bit integer)
- Z = AOUT == 0
- H = (AIN % 16) - (Op % 16) < 0
- P/V = (DiffSIGNED < -128) || (DiffSIGNED > 127)
- N = 1
- C = Diff < 0

---
Let’s De-accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld a,42
ld b,57
sub b
sub b
ld b,180
sub b
sub b
sub b
sub b
ld b,110
sub b
ld b,122
sub b

---
Let’s De-accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,57
sub b
sub b
ld b,180
sub b
sub b
sub b
sub b
ld b,110
sub b
ld b,122
sub b

---
Let’s De-accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,57	42	42	2A	57	57	39	?	?	?	?	?	?
sub b
sub b
ld b,180
sub b
sub b
sub b
sub b
ld b,110
sub b
ld b,122
sub b

---
Let’s De-accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,57	42	42	2A	57	57	39	?	?	?	?	?	?
sub b	241	-15	F1	57	57	39	1	0	0	0	1	1
sub b
ld b,180
sub b
sub b
sub b
sub b
ld b,110
sub b
ld b,122
sub b

---
Let’s De-accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,57	42	42	2A	57	57	39	?	?	?	?	?	?
sub b	241	-15	F1	57	57	39	1	0	0	0	1	1
sub b	184	-72	B8	57	57	39	1	0	1	0	1	0
ld b,180
sub b
sub b
sub b
sub b
ld b,110
sub b
ld b,122
sub b

---
Let’s De-accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,57	42	42	2A	57	57	39	?	?	?	?	?	?
sub b	241	-15	F1	57	57	39	1	0	0	0	1	1
sub b	184	-72	B8	57	57	39	1	0	1	0	1	0
ld b,180	184	-72	B8	180	-76	B4	1	0	1	0	1	0
sub b
sub b
sub b
sub b
ld b,110
sub b
ld b,122
sub b

---
Let’s De-accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,57	42	42	2A	57	57	39	?	?	?	?	?	?
sub b	241	-15	F1	57	57	39	1	0	0	0	1	1
sub b	184	-72	B8	57	57	39	1	0	1	0	1	0
ld b,180	184	-72	B8	180	-76	B4	1	0	1	0	1	0
sub b	4	4	04	180	-76	B4	0	0	0	0	1	0
sub b
sub b
sub b
ld b,110
sub b
ld b,122
sub b

---
Let’s De-accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,57	42	42	2A	57	57	39	?	?	?	?	?	?
sub b	241	-15	F1	57	57	39	1	0	0	0	1	1
sub b	184	-72	B8	57	57	39	1	0	1	0	1	0
ld b,180	184	-72	B8	180	-76	B4	1	0	1	0	1	0
sub b	4	4	04	180	-76	B4	0	0	0	0	1	0
sub b	80	80	50	180	-76	B4	0	0	0	0	1	1
sub b
sub b
ld b,110
sub b
ld b,122
sub b

---
Let’s De-accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,57	42	42	2A	57	57	39	?	?	?	?	?	?
sub b	241	-15	F1	57	57	39	1	0	0	0	1	1
sub b	184	-72	B8	57	57	39	1	0	1	0	1	0
ld b,180	184	-72	B8	180	-76	B4	1	0	1	0	1	0
sub b	4	4	04	180	-76	B4	0	0	0	0	1	0
sub b	80	80	50	180	-76	B4	0	0	0	0	1	1
sub b	156	-100	9C	180	-76	B4	1	0	1	1	1	1
sub b
ld b,110
sub b
ld b,122
sub b

---
Let’s De-accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,57	42	42	2A	57	57	39	?	?	?	?	?	?
sub b	241	-15	F1	57	57	39	1	0	0	0	1	1
sub b	184	-72	B8	57	57	39	1	0	1	0	1	0
ld b,180	184	-72	B8	180	-76	B4	1	0	1	0	1	0
sub b	4	4	04	180	-76	B4	0	0	0	0	1	0
sub b	80	80	50	180	-76	B4	0	0	0	0	1	1
sub b	156	-100	9C	180	-76	B4	1	0	1	1	1	1
sub b	232	-24	E8	180	-76	B4	1	0	0	0	1	1
ld b,110
sub b
ld b,122
sub b

---
Let’s De-accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,57	42	42	2A	57	57	39	?	?	?	?	?	?
sub b	241	-15	F1	57	57	39	1	0	0	0	1	1
sub b	184	-72	B8	57	57	39	1	0	1	0	1	0
ld b,180	184	-72	B8	180	-76	B4	1	0	1	0	1	0
sub b	4	4	04	180	-76	B4	0	0	0	0	1	0
sub b	80	80	50	180	-76	B4	0	0	0	0	1	1
sub b	156	-100	9C	180	-76	B4	1	0	1	1	1	1
sub b	232	-24	E8	180	-76	B4	1	0	0	0	1	1
ld b,110	232	-24	E8	110	110	6E	1	0	0	0	1	1
sub b
ld b,122
sub b

---
Let’s De-accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,57	42	42	2A	57	57	39	?	?	?	?	?	?
sub b	241	-15	F1	57	57	39	1	0	0	0	1	1
sub b	184	-72	B8	57	57	39	1	0	1	0	1	0
ld b,180	184	-72	B8	180	-76	B4	1	0	1	0	1	0
sub b	4	4	04	180	-76	B4	0	0	0	0	1	0
sub b	80	80	50	180	-76	B4	0	0	0	0	1	1
sub b	156	-100	9C	180	-76	B4	1	0	1	1	1	1
sub b	232	-24	E8	180	-76	B4	1	0	0	0	1	1
ld b,110	232	-24	E8	110	110	6E	1	0	0	0	1	1
sub b	122	122	7A	110	110	6E	0	0	1	1	1	0
ld b,122
sub b

---
Let’s De-accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,57	42	42	2A	57	57	39	?	?	?	?	?	?
sub b	241	-15	F1	57	57	39	1	0	0	0	1	1
sub b	184	-72	B8	57	57	39	1	0	1	0	1	0
ld b,180	184	-72	B8	180	-76	B4	1	0	1	0	1	0
sub b	4	4	04	180	-76	B4	0	0	0	0	1	0
sub b	80	80	50	180	-76	B4	0	0	0	0	1	1
sub b	156	-100	9C	180	-76	B4	1	0	1	1	1	1
sub b	232	-24	E8	180	-76	B4	1	0	0	0	1	1
ld b,110	232	-24	E8	110	110	6E	1	0	0	0	1	1
sub b	122	122	7A	110	110	6E	0	0	1	1	1	0
ld b,122	122	122	7A	122	122	7A	0	0	1	1	1	0
sub b

---
Let’s De-accumulate
Instruction	A (unsigned)	A (signed)	A (hex)	B (unsigned)	B (signed)	B (hex)	S	Z	H	P/V	N	C
ld b,57	42	42	2A	57	57	39	?	?	?	?	?	?
sub b	241	-15	F1	57	57	39	1	0	0	0	1	1
sub b	184	-72	B8	57	57	39	1	0	1	0	1	0
ld b,180	184	-72	B8	180	-76	B4	1	0	1	0	1	0
sub b	4	4	04	180	-76	B4	0	0	0	0	1	0
sub b	80	80	50	180	-76	B4	0	0	0	0	1	1
sub b	156	-100	9C	180	-76	B4	1	0	1	1	1	1
sub b	232	-24	E8	180	-76	B4	1	0	0	0	1	1
ld b,110	232	-24	E8	110	110	6E	1	0	0	0	1	1
sub b	122	122	7A	110	110	6E	0	0	1	1	1	0
ld b,122	122	122	7A	122	122	7A	0	0	1	1	1	0
sub b	0	0	00	122	122	7A	0	1	0	0	1	0

---
ADC: ADd with Carry (8-Bit)
- Adds values of second operand and carry bit to accumulator
- First Operand: Always A
- Second Operand:
  - Register:
    - A, B, C, D, E, H, L, IXH, IXL, IYH, IYL
  - Register Indirect:
    - (HL)
  - Indexed:
    - (IX+n), (IY+n)
  - Immediate
    - Example: adc a,42

---
ADC (8-Bit) Effects
- Sum = AIN + Op2 + CIN
- AOUT = Sum % 256
- S = AOUT > 127 (negative if A interpreted as signed 8-bit integer)
- Z = AOUT == 0
- H = (AIN % 16) + (Op2 % 16) > 15
- P/V = (SumSIGNED < -128) || (SumSIGNED > 127)
  - Sum of two “negative” or two “positive” values doesn’t fit A
- N = 0
- COUT = Sum > 255

---
Chaining 8-Bit Additions
- Start with ADD between lowest bytes
- ADC each higher pair of bytes
- Example (HL = BC + DE):
  ld a,c
  add a,e
  ld l,a
  ld a,b
  adc a,d
  ld h,a

---
SBC: SuBtract with Carry (8-bit)
- Subtracts values of second operand and carry bit from accumulator
- First Operand: Always A
- Second Operand:
  - Register:
    - A, B, C, D, E, H, L, IXH, IXL, IYH, IYL
  - Register Indirect:
    - (HL)
  - Indexed:
    - (IX+n), (IY+n)
  - Immediate
    - Example: sbc a,42

---
SBC (8-Bit) Effects
- Diff = AIN – Op2 – CIN
- AOUT = Diff & 255
- S = AOUT > 127 (negative if A interpreted as signed 8-bit integer)
- Z = AOUT == 0
- H = (AIN % 16) - (Op2 % 16) < 0
- P/V = (DiffSIGNED < -128) || (DiffSIGNED > 127)
- N = 1
- COUT = Diff < 0

---
Chaining 8-Bit Subtractions
- Start with SUB between lowest bytes
- SBC each higher pair of bytes
- Example (HL = BC - DE):
  ld a,c
  sub e
  ld l,a
  ld a,b
  sbc a,d
  ld h,a

---
ADD (16-Bit)
- Adds value of second operand to first operand
- First Operand: HL, IX, IY
- Second Operand: BC, DE, SP, First Operand (HL, IX, IY)
- Example (HL = BC + DE):
  ld h,b
  ld l,c
  add hl,de
  - 3 bytes and 19 T-states
  - 8-bit Chaining: 6 bytes and 24 T-states

---
ADD (16-Bit) Effects
- Sum = Op1IN + Op2
- Op1OUT = Sum % 65,536
- H = ? (Undefined)
- N = 0
- C = Sum > 65,535
- Preserves S, Z, P/V

---
ADC: ADd with Carry (16-Bit)
- Adds values of second operand and carry bit to HL
- First Operand: Always HL
- Second Operand: BC, DE, HL, SP
- Sum = HLIN + Op2 + CIN
- HLOUT = Sum % 65,535
- H = ? (Undefined)
- N = 0
- C = Sum > 65,535
- Preserves S, Z, P/V

---
SBC: SuBtract with Carry (16-bit)
- Subtracts values of second operand and carry bit from HL
- First Operand: Always HL
- Second Operand: BC, DE, HL, SP
- Example (HL = BC - DE):
  ld h,b
  ld l,c
  cp a ; clears C
  sbc hl,de
  - 4 bytes and 27 T-states
  - 8-bit Chaining: 6 bytes and 24 T-states

---
SBC (16-Bit) Effects
- Diff = HLIN – Op2 – CIN
- HLOUT = Diff % 65,536
- S = HLOUT > 32,767 (negative if A interpreted as signed)
- Z = HLOUT == 0
- H = ? (Undefined)
- P/V = (DiffSIGNED < -32,768) || (DiffSIGNED > 32,767)
- N = 1
- COUT = Diff < 0

---
INC: INCrement
- Adds 1 to the value of the operand
- Register
  - 8-bit: A, B, C, D, E, H, L, IXH, IXL, IYH, IYL
  - 16-bit: BC, DE, HL, IX, IY, SP
- Register Indirect
  - (HL)
- Indexed
  - (IX+n), (IY+n)

---
INC Effects
- OpOUT = OpIN + 1
- 8-Bit:
  - C flag preserved
  - Other flags same effects as 8-bit ADD/ADC
- 16-Bit:
  - All flags preserved

---
DEC: DECrement
- Subtracts 1 from the value of the operand
- Register
  - 8-bit: A, B, C, D, E, H, L, IXH, IXL, IYH, IYL
  - 16-bit: BC, DE, HL, IX, IY, SP
- Register Indirect
  - (HL)
- Indexed
  - (IX+n), (IY+n)

---
DEC Effects
- OpOUT = OpIN - 1
- 8-Bit:
  - C flag preserved
  - Other flags same effects as 8-bit SUB/SBC
- 16-Bit:
  - All flags preserved

---
NEG: NEGate
- Negates the value in the accumulator
- AOUT = 0 – AIN
- S = AOUT > 127
- Z = AOUT == 0
- H = (AIN % 16) > 0
- P/V = AIN == 128
- N = 1
- C = AIN > 0

---
Example Program
- Do some math!
- Use different instructions and addressing modes
- Print register contents in hex