Z80 Assembly
for the
Lesson 9: The Rest

---
NOP: No OPeration
- No operands
- No flags affected
- Executed in 4 T-States

---
DAA: Decimal Adjust Accumulator
- Adjusts value in A after Binary-Coded Decimal (BCD) operation
- If (A & $0F) > 9 OR H flag is set:
  - A = A + $06
- If (A > $9F) OR C flag is set:
  - A = A + $60
  - Set C flag
- Else
  - Clear C flag

---
CPI: ComPare and Increment
- Forward search iteration:
  cp (hl)
  inc hl
  dec bc
- Z = A == (HL) before HL incremented
- P/V = Overflow on BC decrement
- N = 1, C bit preserved
- 16 T-States (vs. 7+6+6=19)

---
CPD: ComPare and Decrement
- Backward search iteration:
  cp (hl)
  dec hl
  dec bc
- Z = A == (HL) before HL decremented
- P/V = Overflow on BC decrement
- N = 1, C bit preserved
- 16 T-States (vs. 7+6+6=19)

---
CPIR: ComPare, Increment and Repeat
- Forward search
  - Repeat CPI until A == (HL-1) or BC == 0
- Z = Search successful before BC decremented to zero
- N = 1, C bit preserved

---
CPDR: ComPare, Decrement and Repeat
- Backward search
  - Repeat CPD until A == (HL+1) or BC == 0
- Z = Search successful before BC decremented to zero
- N = 1, C bit preserved

---
IM: Interrupt Mode
- One operand: 0, 1 or 2
- IM 0
  - Instruction opcode placed on data bus by interrupting device
  - Not supported by ZX Spectrum
- IM 1
  - Always jump to service routine at $0038
  - Default for ZX Spectrum on boot to BASIC
- IM 2
  - Jump to address in table, on page specified by I register, offset placed on data bus.

---
EI: Enable Interrupt
- Enables maskable interrupts for last specified mode
  - Maskable interrupts disabled during non-maskable interrupt (NMI) service
- No flags affected

---
DI: Disable Interrupt
- Disables maskable interrupts (any mode)
- Does not affect NMI (always enabled)
- No flags affected

---
HALT
- Stops execution until next interrupt
  - NMI or maskable interrupt
- Execution resumes with following instruction after interrupt serviced

---
Example Program
- Demonstrate use of NOP, DAA, CPIR, CPDR
  - BCD Addition
  - Code Search