Z80 Assembly
for the
Lesson 8: In and Out

---
Z80 Ports
Z80
ADDRESS
|
16
DATA
|
8
MREQ
IOREQ
Memory
EN
ULA
EN

---
IN
- First Operand: Destination of data
  - Register: A, B, C, D, E, H, L
- Second Operand: Port Address (7:0)
  - Direct: Low byte hard-coded, High byte in A
    - First operand must be A
    - Example:
      ld a,$F7
      in a,($FE) ; A ← Port $F7FE
  - Register Indirect: Address in BC
    - Example:
      ld bc,$BFFE
      in d,(c) ; D ← Port $BFFE
    - N = 0; H = 0; P/V = Parity; S = Op1 bit 7; Z = Op1 == 0

---
Keyboard Input

---
IN
- First Operand: Destination of data
  - Register: A, B, C, D, E, H, L
- Second Operand: Port Address (7:0)
  - Direct: Low byte hard-coded, High byte in A
    - First operand must be A
    - Example:
      ld a,$F7
      in a,($FE) ; A ← Port $F7FE
  - Register Indirect: Address in BC
    - Example:
      ld bc,$BFFE
      in d,(c) ; D ← Port $BFFE
    - N = 0; H = 0; P/V = Parity; S = Op1 bit 7; Z = Op1 == 0

---
Example Program
- Perform bitwise operations
- Print register contents