Z80 Assembly
for the
Lesson 6: The Stack

---
Z80 Architecture
A
F
A’
F’
B
C
B’
C’
D
E
D’
E’
H
L
H’
L’
SP
PC
IX
IY
I
R

---
ZX Spectrum 48k Memory Map
0000	ROM	16 kB
3FFF
4000	Screen Bitmap (256x192)	6 kB
57FF
5800	Screen Color Attributes (32x24)	768 Bytes
5AFF
5B00	Reserved for BASIC	1.20 kB
5CCA
5CCB	Contended User RAM	8.80 kB
7FFF
8000	Free User RAM	31.84 kB
FF57
FF58	User-Defined Graphics (UDG)	168 Bytes
FFFF

---
Stack Behavior
- SP: 16-bit Stack Pointer (to RAM)
- PUSH: Decrement SP by 2 and store word there
- POP: Load word at SP, then increment by 2
STACK
FF53	??
FF54	??
FF55	??
FF56	??
FF57	??
FF58	00
   org $8000
   ld hl,$FF58
   ld sp,hl
   push hl
   call foo
   pop hl
   halt
foo:
   ld hl,$1234
   ret
REGISTERS
PC	SP	H	L
8000	????	??	??

---
Stack Behavior
- SP: 16-bit Stack Pointer (to RAM)
- PUSH: Decrement SP by 2 and store word there
- POP: Load word at SP, then increment by 2
STACK
FF53	??
FF54	??
FF55	??
FF56	??
FF57	??
FF58	00
   org $8000
   ld hl,$FF58
   ld sp,hl
   push hl
   call foo
   pop hl
   halt
foo:
   ld hl,$1234
   ret
REGISTERS
PC	SP	H	L
8003	????	FF	58

---
Stack Behavior
- SP: 16-bit Stack Pointer (to RAM)
- PUSH: Decrement SP by 2 and store word there
- POP: Load word at SP, then increment by 2
STACK
FF53	??
FF54	??
FF55	??
FF56	??
FF57	??
FF58	00
   org $8000
   ld hl,$FF58
   ld sp,hl
   push hl
   call foo
   pop hl
   halt
foo:
   ld hl,$1234
   ret
REGISTERS
PC	SP	H	L
8004	FF58	FF	58

---
Stack Behavior
- SP: 16-bit Stack Pointer (to RAM)
- PUSH: Decrement SP by 2 and store word there
- POP: Load word at SP, then increment by 2
STACK
FF53	??
FF54	??
FF55	??
FF56	58
FF57	FF
FF58	00
   org $8000
   ld hl,$FF58
   ld sp,hl
   push hl
   call foo
   pop hl
   halt
foo:
   ld hl,$1234
   ret
REGISTERS
PC	SP	H	L
8005	FF56	FF	58

---
Stack Behavior
- SP: 16-bit Stack Pointer (to RAM)
- PUSH: Decrement SP by 2 and store word there
- POP: Load word at SP, then increment by 2
STACK
FF53	??
FF54	08
FF55	80
FF56	58
FF57	FF
FF58	00
   org $8000
   ld hl,$FF58
   ld sp,hl
   push hl
   call foo
   pop hl
   halt
foo:
   ld hl,$1234
   ret
REGISTERS
PC	SP	H	L
800A	FF54	FF	58

---
Stack Behavior
- SP: 16-bit Stack Pointer (to RAM)
- PUSH: Decrement SP by 2 and store word there
- POP: Load word at SP, then increment by 2
STACK
FF53	??
FF54	08
FF55	80
FF56	58
FF57	FF
FF58	00
   org $8000
   ld hl,$FF58
   ld sp,hl
   push hl
   call foo
   pop hl
   halt
foo:
   ld hl,$1234
   ret
REGISTERS
PC	SP	H	L
800D	FF54	12	34

---
Stack Behavior
- SP: 16-bit Stack Pointer (to RAM)
- PUSH: Decrement SP by 2 and store word there
- POP: Load word at SP, then increment by 2
STACK
FF53	??
FF54	08
FF55	80
FF56	58
FF57	FF
FF58	00
   org $8000
   ld hl,$FF58
   ld sp,hl
   push hl
   call foo
   pop hl
   halt
foo:
   ld hl,$1234
   ret
REGISTERS
PC	SP	H	L
8008	FF56	12	34

---
Stack Behavior
- SP: 16-bit Stack Pointer (to RAM)
- PUSH: Decrement SP by 2 and store word there
- POP: Load word at SP, then increment by 2
STACK
FF53	??
FF54	08
FF55	80
FF56	58
FF57	FF
FF58	00
   org $8000
   ld hl,$FF58
   ld sp,hl
   push hl
   call foo
   pop hl
   halt
foo:
   ld hl,$1234
   ret
REGISTERS
PC	SP	H	L
8009	FF58	FF	58

---
CALL Effects
- Unconditional:
  - PCOUT = operand
- Conditional and taken:
  - PCOUT = second operand
- Unconditional OR conditional and taken:
  - SPOUT = SPIN – 2
  - (SPOUT) = PCIN + 3
- Conditional and not taken:
  - PCOUT = PCIN + 3

---
RST – call ReSeT vector
- Shortcut for calling special routines on page zero
- Operand: 8-bit address (upper byte zero)
  - Supported Addresses: $00, $08, $10, $18, $20, $28, $30, $38
- Effects:
  - PCOUT = operand
  - SPOUT = SPIN – 2
  - (SPOUT) = PCIN + 1

---
RET Effects
- Unconditional OR conditional and taken:
  - PCOUT = (SPIN)
  - SPOUT = SPIN + 2
- Conditional and not taken:
  - PCOUT = PCIN + 3

---
PUSH
- Pushes register value to stack
- Supported registers: AF, BC, DE, HL, IX, IY
- Example: push hl
  - Effects:
    - SPOUT = SPIN – 2
    - (SPOUT) = L
    - (SPOUT + 1) = H

---
POP
- Pops value off stack, stores it in register
- Supported registers: AF, BC, DE, HL, IX, IY
- Example: pop hl
  - Effects:
    - L = (SPIN)
    - H = (SPIN + 1)
    - SPOUT = SPIN + 2
- Flags unaffected unless AF is popped, and flag values are retrieved from stack

---
Example Program
- Re-map the stack to screen memory
- Render stripe pattern