Z80 Assembly
for the
Lesson 12: Interrupts

---
A Tale of Two Interrupts
- Normal execution on the Z80 can be interrupted by one of two pins being held low during a rising clock edge.
- If enabled, INT triggers a
  maskable interrupt
- NMI always triggers a
  non-maskable interrupt
- NMI can interrupt maskable
  interrupt service routine, but
  not vice versa

---
Interrupts on the ZX Spectrum
- INT is tied to ULA, triggered at beginning of video vertical blanking period.
  - 7-8 lines per field
    - 448-512 μs
    - 1568-1792 T-States @ 3.5 MHz
- NMI is held high unless connected through expansion port.
  - Will always execute NMI routine at $0066
  - Expansion may override ROM on models
    earlier than ZX Spectrum +3

---
IM: Interrupt Mode
- One operand: 0, 1 or 2
- IM 0
  - Instruction opcode placed on data bus by interrupting device
  - Not supported by ZX Spectrum
- IM 1
  - Always jump to service routine at $0038
  - Default for ZX Spectrum on boot to BASIC
- IM 2
  - Jump to address in table, on page specified by I register, offset placed on data bus.
unless through expansion port
The ULA only reads from data bus

---
EI: Enable Interrupt
- No operands
- Enables maskable interrupts for last specified mode
  - Maskable interrupts disabled during non-maskable interrupt (NMI) service
- No flags affected
- IFF1 and IFF2 flip-flops are set to enabled
  - Maskable interrupts disabled when IFF1 reset
  - IFF1 reset when NMI triggered, restored to state of IFF2 after RETN (i.e. Maskable interrupts will be enabled again if they were at the time of the NMI and not disabled with DI since)

---
DI: Disable Interrupt
- No operands
- Disables maskable interrupts (any mode)
- Does not affect NMI (always enabled)
- No flags affected
- IFF1 and IFF2 flip-flops are both reset
  - EI must be executed again to re-enable interrupts
    - Maskable interrupt automatically resets IFF1 and IFF2
      - EI required to re-enable
    - DI during NMI will be permanent until next EI

---
ZX Spectrum 48k Memory Map
0000	ROM	16 kB
3FFF
4000	Screen Bitmap (256x192)	6 kB
57FF
5800	Screen Color Attributes (32x24)	768 Bytes
5AFF
5B00	Reserved for BASIC	1.20 kB
5CCA
5CCB	Contended User RAM	8.80 kB
7FFF
8000	Free User RAM	31.84 kB
FF57
FF58	User-Defined Graphics (UDG)	168 Bytes
FFFF
IM 1: $0038
IM 2: Any
Page + 1B

---
IM 1 Service Routine
- $0038 in ROM
  - Preserve AF, HL, BC, DE on stack
  - Increment 24-bit frame counter ($5C78)
  - Scan keyboard (CALL $02BF)
    - If key pressed:
      - Place code in LAST-K ($5C08)
      - Handle repeats
  - Restore DE, BC, HL, AF from stack
  - Enable Interrupts (EI)
  - Return (RET, not RETI)

---
IM 2 Service Routine
- Page of vector: I register
- Offset of vector: value on data bus (effectively random if ULA interrupt for vertical blank)
- Solution: vector page all same value, plus first byte of next page.
  - Requires vector address value to have matching high and low bytes
  - Least Intrusive Example:
    - Load $FE into I
    - Fill $FE00-FF00 with $FD
    - Place JP to RAM routine at $FDFD

---
Example Program
Move a “sprite” right and left using X and Z keys