Z80 Assembly
for the
Lesson 3: Data in Motion

---
“Load” Mnemonic Syntax
LD destination,source
; Assembly: C:
  ld a,42 ; A = 42
  ld ($89AB),a ; *(0x89AB) = A
  ld (hl),d ; *HL = D
  ld bc,($CDEF) ; BC = *(0xCDEF)
  ld a,(bc) ; A = *BC

---
Z80 Architecture
A
F
A’
F’
B
C
B’
C’
D
E
D’
E’
H
L
H’
L’
SP
PC
IX
IY
I
R

---
ZX Spectrum 48k Memory Map
0000	ROM	16 kB
3FFF
4000	Screen Bitmap (256x192)	6 kB
57FF
5800	Screen Color Attributes (32x24)	768 Bytes
5AFF
5B00	Reserved for BASIC	1.20 kB
5CCA
5CCB	Contended User RAM	8.80 kB
7FFF
8000	Free User RAM	31.84 kB
FF57
FF58	User-Defined Graphics (UDG)	168 Bytes
FFFF

---
Hardware Ports
- Input/Output devices mapped to 8-bit Port Addresses
  - Port Address: Lower 8-bits of address bus
  - Upper 8-bits of address bus may also be used during I/O request
- ULA: Port $FE
  - Keyboard
  - Tape I/O
  - Piezoelectric Beeper

---
LD: LoaD
- Operands: Destination, Source
- 181 Opcodes!
- 8-bit Register-to-Register:
Source
101!
Destination

---
LD: LoaD
- 16-bit Register-to-Register:
  - ld sp,hl	ld sp,ix	ld sp,iy
- Immediate Loads:
  - Example: ld a,42
  - Other destinations: B, C, D, E, H, L, IXH, IXL, IYH, IYL
- Extended Immediate Loads:
  - Example: ld bc,1323
  - Other destinations: DE, HL, SP, IX, IY

---
LD: LoaD
- 8-Bit Direct to Register:
  - Example: ld a,($1234)
  - No other destinations
- 16-Bit Direct to Register:
  - Example: ld bc,($5678)
  - Other destinations: DE, HL, SP, IX, IY

---
LD: LoaD
- 8-Bit Register to Direct:
  - Example: ld ($1234),a
  - No other sources
- 16-Bit Register to Direct:
  - Example: ld ($5678),bc
  - Other sources: DE, HL, SP, IX, IY

---
LD: LoaD
- Register Indirect to Register
  - To A only: ld a,(bc)	ld a,(de)
  - From (HL):
    - Example: ld a,(hl)
    - Other destinations: B, C, D, E, H, L
- Register to Register Indirect:
  - From A only: ld (bc),a	ld (de),a
  - To (HL):
    - Example: ld (hl),a
    - Other sources: B, C, D, E, H, L

---
LD: LoaD
- Register to Indexed
  - To (offset from IX):
    - Example: ld (ix+57),a
    - Other sources: B, C, D, E, H, L
  - To (offset from IY):
    - Example: ld (iy-103),a
    - Other sources: B, C, D, E, H, L
- Indexed to Register
  - From (offset from IX):
    - Example: ld a,(ix+57)
    - Other destinations: B, C, D, E, H, L
  - From (offset from IY):
    - Example: ld a,(iy-103)
    - Other destinations: B, C, D, E, H, L

---
EX: EXchange
- Operands: Two 16-bit locations
- Locations exchange values
- 5 opcodes:
  - ex af,af’
  - ex de,hl
  - ex (sp),hl
  - ex (sp),ix
  - ex (sp),iy

---
EXX: EXchange X
- No operands
- 3 16-bit registers exchange values with alternates
- Results:
  - BC ↔ BC’
  - DE ↔ DE’
  - HL ↔ HL’

---
Using Alternate Registers
Alternate registers can’t be operated on directly
Instruction	A	BC	DE	HL	A’	BC’	DE’	HL’
ld a,42	42	?	?	?	?	?	?	?
ex af,af’	?	?	?	?	42	?	?	?
ld a,57	57	?	?	?	42	?	?	?
ex af,af’	42	?	?	?	57	?	?	?
ld bc,6502	42	6502	?	?	57	?	?	?
ld de,768	42	6502	768	?	57	?	?	?
ld hl,22528	42	6502	768	22528	57	?	?	?
exx	42	?	?	?	57	6502	768	22528
ld bc,8080	42	8080	?	?	57	6502	768	22528
ld de,6144	42	8080	6144	?	57	6502	768	22528
ld hl,16384	42	8080	6144	16384	57	6502	768	22528
exx	42	6502	768	22528	57	8080	6144	16384

---
LDI: Load-Increment
- No operands
- Copies byte value from one memory address to another
- Increments both address registers
- Decrements byte count register
- Operation:
  (DE) = (HL)
  DE = DE + 1
  HL = HL + 1
  BC = BC - 1

---
LDIR: Load-Increment-Repeat
- No operands
- Copies data block to new memory location
- Operation:
  repeat:
    LDI
  until BC == 0
- Spoiler Alert: This could take a while!

---
Copying Data Block
Copy full 6912-byte screen buffer from $E000 to screen memory ($4000)
ld bc,6912
ld de,$4000
ld hl,$E000
ldir

---
LDD: Load-Decrement
- No operands
- Copies byte value from one memory address to another
- Decrements both address registers and byte count register
- Operation:
  (DE) = (HL)
  DE = DE - 1
  HL = HL - 1
  BC = BC - 1

---
LDDR: Load-Decrement-Repeat
- No operands
- Copies data block to new memory location
- Reverse order and direction from LDIR
- Operation:
  repeat:
    LDD
  until BC == 0
- Spoiler Alert: This could also take a while!

---
Copying Data Block – Backwards!
Copy full 6912-byte screen buffer from $E000 to screen memory ($4000), starting from end of buffer
ld bc,6912
ld de,$5AFF ; $4000 + 6911
ld hl,$FAFF ; $E000 + 6911
lddr

---
Example Program
Use LD, EX, EXX, LDI, LDD, LDIR, LDDR to create and move data around