Z80 Assembly
for the
Lesson 8: In and Out

---
Z80 Ports
Z80
ADDRESS
|
16
DATA
|
8
MREQ
IOREQ
Memory
EN
ULA
EN

---
IN
- First Operand: Destination of data
  - Register: A, B, C, D, E, H, L
- Second Operand: Port Address (7:0)
  - Direct: Low byte hard-coded, High byte in A
    - First operand must be A
    - Example:
      ld a,$F7
      in a,($FE) ; A ← Port $F7FE
  - Register Indirect: Address in BC
    - Example:
      ld bc,$BFFE
      in d,(c) ; D ← Port $BFFE
    - N = 0; H = 0; P/V = Parity; S = Op1 bit 7; Z = Op1 == 0

---
Keyboard Input
Port	Bit 4	Bit 3	Bit 2	Bit 1	Bit 0
$7FFE	B	N	M	Symbol / Shift	Space
$BFFE	H	J	K	L	Enter
$DFFE	Y	U	I	O	P
$EFFE	6	7	8	9	0
$F7FE	5	4	3	2	1
$FBFE	T	R	E	W	Q
$FDFE	G	F	D	S	A
$FEFE	V	C	X	Z	Caps / Shift
Example:
   ld bc,$FEFE
   in d,(c)
   bit 0,d
   ret nz
   ld b,$7F
   in e,(c)
   bit 2,e
   call z,handle_shift_m
   ret

---
Keyboard Example
Store all key states in B, C, D, E, B’, C’, D’ and E’
ld a,$FE
   in a,($FE)
   ld bc,$FDFE
   ld b,$FB
   ld b,$F7
   in h,(c)
   ld b,$EF
   in l,(c)
   ld b,h
   ld c,l
   exx
   ld bc,$DFFE
   ld b,$BF
   ld c,a
A:
B:
C:
D:
E:
B’:
C’:
D’:
E’:
?
?
?
?
?
?
?
?
?

---
$FE
?
?
?
?
?
?
?
?

---
[V,C,X,Z,Shift]
?
?
?
?
?
?
?
?

---
[V,C,X,Z,Shift]
$FD
$FE
[G,F,D,S,A]
?
?
?
?
?

---
[V,C,X,Z,Shift]
$FB
$FE
[G,F,D,S,A]
[T,R,E,W,Q]
?
?
?
?

---
[V,C,X,Z,Shift]
[5,4,3,2,1]
[6,7,8,9,0]
[G,F,D,S,A]
[T,R,E,W,Q]
?
?
?
?

---
[V,C,X,Z,Shift]
?
?
?
?
[5,4,3,2,1]
[6,7,8,9,0]
[G,F,D,S,A]
[T,R,E,W,Q]

---
[V,C,X,Z,Shift]
$DF
$FE
[Y,U,I,O,P]
?
[5,4,3,2,1]
[6,7,8,9,0]
[G,F,D,S,A]
[T,R,E,W,Q]

---
[V,C,X,Z,Shift]
$BF
$FE
[Y,U,I,O,P]
[H,J,K,L,Enter]
[5,4,3,2,1]
[6,7,8,9,0]
[G,F,D,S,A]
[T,R,E,W,Q]

---
[V,C,X,Z,Shift]
[B,N,M,Sym,Space]
$FE
[Y,U,I,O,P]
[H,J,K,L,Enter]
[5,4,3,2,1]
[6,7,8,9,0]
[G,F,D,S,A]
[T,R,E,W,Q]

---
[V,C,X,Z,Shift]
[B,N,M,Sym,Space]
[V,C,X,Z,Shift]
[Y,U,I,O,P]
[H,J,K,L,Enter]
[5,4,3,2,1]
[6,7,8,9,0]
[G,F,D,S,A]
[T,R,E,W,Q]

---
OUT
- First Operand: Port Address (7:0)
  - Direct: Low byte hard-coded, High byte in A
    - Second operand must be A
    - Example:
      ld a,$10
      out ($FE),a ; $10 → Port $10FE
  - Register Indirect: Address in BC
    - Example:
      ld bc,$1FFD
      out (c),d ; D → Port $1FFD
- Second Operand: Source of data
  - Register: A, B, C, D, E, H, L
...or zero
UNDOCUMENTED

---
Sound Output
- Piezoelectric beeper controlled by bit 4 of port $FE
- Middle C = 261.6 Hz
  - Period: 3.8226 ms (13,380 T-states @ 3.5 MHz)
  - Output $10 for 6,690 T-states, zero for 6,690, repeat
- For Spectrum 128k: AY-3-8912 controlled by ports $BFFD, $FFFD
  - Read/write registers
  - Set channels to notes

---
Sound Example
- Play 100 Hz tone
- Just flip bit 4 on $FE after every PAL frame (50 Hz) interrupt
  ei
  ld c,$fe
sound_loop:
   xor $10
   halt
   out (c),a
   jp sound_loop

---
IN Loop Instructions
- INI: INput and Increment
  - Same as:
    in (hl),(c)
    inc hl
    dec b
- INIR: INput, Increment, Repeat
  - Same as:
    ini_loop:
    ini
    jp nz,ini_loop
- IND: INput and Decrement
  - Same as:
    in (hl),(c)
    dec hl
    dec b
- INDR: INput, Decrement, Repeat
  - Same as:
    ind_loop:
    ind
    jp nz,ind_loop

---
OUT Loop Instructions
- OUTD: OUTput and Decrement
  - Same as:
    out (c),(hl)
    dec hl
    dec b
- OTDR: OUTput, Decrement, Repeat
  - Same as:
    outd_loop:
    outd
    jp nz,outd_loop
- OUTI: OUTput and Increment
  - Same as:
    out (c),(hl)
    inc hl
    dec b
- OTIR: OUTput, Increment, Repeat
  - Same as:
    outi_loop:
    outi
    jp nz,outi_loop

---
Example Program
- Play tone while X key is pressed
- Embedded applications need no screenshots!