Z80 Assembly
for the
Lesson 4: Conditionality

---
Z80 Status Flags
S	Z	B5	H	B3	P/V	N	C
- F Register:
  - S: Signed – Value in A is negative
  - Z: Zero – Value in A is zero
  - B5: Bit 5 of last 8-bit opcode that altered flags
  - H: Half-Carry – Overflow occurred with lower nybble
  - B3: Bit 3 of last 8-bit opcode that altered flags
  - P/V: Parity/Overflow – Parity bit or overflow occurred
  - N: Add/Subtract – Subtract occurred since last add
  - C: Carry – Bit to carry to next operation

---
Z80 Status Flags
S	Z	B5	H	B3	P/V	N	C
- F Register:
  - S: Signed – Value in A is negative
  - Z: Zero – Value in A is zero
  - B5: Bit 5 of last 8-bit opcode that altered flags
  - H: Half-Carry – Overflow occurred with lower nybble
  - B3: Bit 3 of last 8-bit opcode that altered flags
  - P/V: Parity/Overflow – Parity bit or overflow occurred
  - N: Add/Subtract – Subtract occurred since last add
  - C: Carry – Bit to carry to next operation

---
Condition Mnemonic
- Used as first operand for all conditional assembly instructions
  - C - carry bit set (C = 1)
  - NC - carry bit reset (C = 0)
  - Z - zero bit set (Z = 1)
  - NZ - zero bit reset (Z = 0)
  - M - sign bit set (S = 1)
  - P - sign bit reset (S = 0)
  - PE - overflow bit set (P/V = 1)
  - PO - overflow bit reset (P/V = 0)

---
JP: JumP
- Jump to absolute address
- Unconditional: Always jump
  - Extended Immediate: jp $89AB
  - Register Indirect: jp (hl) . jp (ix) . jp (iy)
- Conditional: Jump if condition is true
  - Supported conditions: C, NC, Z, NZ, M, P, PE, PO
  - Target must be Extended Immediate address
  - Example: jp nz,$CDEF

---
Simple Looping
- Initialize loop index, decrement until Z bit set
- Case Study: Multiply value in accumulator by 32 (25)
  ld b,5
  loop:
  sla a
  dec b
  jp nz,loop

---
JR: Jump Relative
- Jump to relative address
  - Target address must be 8-bit offset from next instruction
- Unconditional: Always jump
  - Example: jr label
- Conditional: Jump if condition is true
  - Supported conditions: C, NC, Z, NZ
  - Example: jr c,label

---
CP: ComPare
- Compares value in accumulator to another
- Sets flags based on sign and comparison
- Register Mode: Compare A with A, B, C, D, E, H, L, IXH, IXL, IYH, IYL
  - Example: cp b
- Immediate Mode: Compare A with 8-bit value
  - Example: cp 42
- Register Indirect: cp (hl)
- Indexed: cp (ix+101) . cp (iy-57)

---
CP: ComPare
- Any comparison (N = value from operand):
  - A == N: Z = 1
  - A != N: Z = 0
- Unsigned comparison:
  - A < N: C = 1
  - A >= N: C = 0
- Signed comparison (S bit = Bit 7 of A):
  - A < N: P/V == S
  - A >= N: P/V != S

---
LD: LoaD
- Register Indirect to Register
  - To A only: ld a,(bc)	ld a,(de)
  - From (HL):
    - Example: ld a,(hl)
    - Other destinations: B, C, D, E, H, L
- Register to Register Indirect:
  - From A only: ld (bc),a	ld (de),a
  - To (HL):
    - Example: ld (hl),a
    - Other sources: B, C, D, E, H, L

---
LD: LoaD
- Register to Indexed
  - To (offset from IX):
    - Example: ld (ix+57),a
    - Other sources: B, C, D, E, H, L
  - To (offset from IY):
    - Example: ld (iy-103),a
    - Other sources: B, C, D, E, H, L
- Indexed to Register
  - From (offset from IX):
    - Example: ld a,(ix+57)
    - Other destinations: B, C, D, E, H, L
  - From (offset from IY):
    - Example: ld a,(iy-103)
    - Other destinations: B, C, D, E, H, L

---
EX: EXchange
- Operands: Two 16-bit locations
- Locations exchange values
- 5 opcodes:
  - ex af,af’
  - ex de,hl
  - ex (sp),hl
  - ex (sp),ix
  - ex (sp),iy

---
EXX: EXchange X
- No operands
- 3 16-bit registers exchange values with alternates
- Results:
  - BC ↔ BC’
  - DE ↔ DE’
  - HL ↔ HL’

---
Using Alternate Registers
Alternate registers can’t be operated on directly
Instruction	A	BC	DE	HL	A’	BC’	DE’	HL’
ld a,42	42	?	?	?	?	?	?	?
ex af,af’	?	?	?	?	42	?	?	?
ld a,57	57	?	?	?	42	?	?	?
ex af,af’	42	?	?	?	57	?	?	?
ld bc,6502	42	6502	?	?	57	?	?	?
ld de,768	42	6502	768	?	57	?	?	?
ld hl,22528	42	6502	768	22528	57	?	?	?
exx	42	?	?	?	57	6502	768	22528
ld bc,8080	42	8080	?	?	57	6502	768	22528
ld de,6144	42	8080	6144	?	57	6502	768	22528
ld hl,16384	42	8080	6144	16384	57	6502	768	22528
exx	42	6502	768	22528	57	8080	6144	16384

---
LDI: LoaD-Increment
- No operands
- Copies byte value from one memory address to another
- Increments both address registers
- Decrements byte count register
- Operation:
  (DE) = (HL)
  DE = DE + 1
  HL = HL + 1
  BC = BC - 1

---
LDIR: LoaD-Increment-Repeat
- No operands
- Copies data block to new memory location
- Operation:
  repeat:
    LDI
  until BC == 0
- Spoiler Alert: This could take a while!

---
Copying Data Block
Copy full 6912-byte screen buffer from $E000 to screen memory ($4000)
ld bc,6912
ld de,$4000
ld hl,$E000
ldir

---
LDD: LoaD-Decrement
- No operands
- Copies byte value from one memory address to another
- Decrements both address registers and byte count register
- Operation:
  (DE) = (HL)
  DE = DE - 1
  HL = HL - 1
  BC = BC - 1

---
LDDR: Load-Decrement-Repeat
- No operands
- Copies data block to new memory location
- Reverse order and direction from LDIR
- Operation:
  repeat:
    LDD
  until BC == 0
- Spoiler Alert: This could also take a while!

---
Copying Data Block – Backwards!
Copy full 6912-byte screen buffer from $E000 to screen memory ($4000), starting from end of buffer
ld bc,6912
ld de,$5AFF ; $4000 + 6911
ld hl,$FAFF ; $E000 + 6911
lddr

---
Example Program
Use LD, EX, EXX, LDI, LDD, LDIR, LDDR to create and move data around